## Slide 1
Hardware/Software Co-Design for
LLM Quantization
Comparing ASIC and FPGA Approaches for Efficient Inference
Gyanendra Pandey
CECS 530 — Advanced Computer Architecture
6th December 2025
1

## Slide 2
Introduction & Background
Large Language Models are Transforming AI
GPT-4, LLaMA, Claude — billions of parameters delivering unprecedented capabilities in text, code, and reasoning.
LLMs
Powerful but huge
→
Memory Wall
140GB+ models
→
Quantization
Shrink weights
→
Hardware Co-Design
Efficient inference
The Challenge
Models too large for available memory
High power consumption (300W/GPU)
Inference cost at scale ($700K/day)
The Opportunity
Quantization reduces memory 2-4×
Custom hardware eliminates overhead
Co-design achieves both goals
This presentation: We analyze how hardware-software co-design approaches (Oltron, FlightLLM) outperform software-only quantization methods.
2

## Slide 3
Motivation
Why Efficient LLM Deployment Matters
$700K
per day
ChatGPT inference cost
300W
per GPU
A100 power consumption
140GB
model size
LLaMA-70B in FP16
Datacenter Impact
Thousands of GPUs running 24/7. Power costs dominate operating expenses. Every efficiency gain multiplies across the fleet.
Accessibility Gap
Consumer GPUs have 8-24GB. Most LLMs don't fit. Quantization + hardware co-design can democratize access.
Environmental
AI training and inference consume significant energy. Efficient deployment reduces carbon footprint at scale.
Bottom line: We need efficient deployment — not just accurate models. Hardware-software co-design addresses both.
3

## Slide 4
The Problem: Memory Wall
LLaMA-70B requires 140 GB of memory
Our laptop has 16 GB. Our GPU has 24 GB. The model doesn't fit.
140 GB
LLaMA-70B
FP16
70 GB
LLaMA-70B
INT8
35 GB
LLaMA-70B
INT4
24 GB
RTX 4090
GPU
16 GB
Laptop
RAM
How Quantization Helps
FP16 → INT8: 2x smaller
FP16 → INT4: 4x smaller
But: Naive quantization breaks model accuracy!
Key point: Quantization reduces precision to shrink model size — but we need smart approaches to maintain accuracy.
4

## Slide 5
What is Quantization?
Reducing numerical precision of model weights and activations to decrease memory and computation.
FP32 (32-bit)
3.14159265...
32 bits per value
Baseline
→
INT8 (8-bit)
3 (integer)
8 bits per value
4× smaller
→
INT4 (4-bit)
3 (integer)
4 bits per value
8× smaller
Benefits
Smaller model size
Faster inference
Lower power usage
Challenges
Precision loss
Outlier sensitivity
Accuracy degradation
Key tradeoff: Lower precision means smaller size, but we risk losing accuracy if not done carefully.
5

## Slide 6
Why Hardware Matters
Key insight: LLM inference is memory-bound, not compute-bound. The GPU sits idle waiting for data.
GPU Architecture Bottleneck
Thousands of GPU Cores (mostly idle)
BOTTLENECK
Memory Bandwidth
A100 GPU Specs:
Compute: 312 TFLOPS
Memory BW: 2 TB/s
LLaMA-70B: Read 140GB per token
Why Quantization Helps (But Not Enough)
Reduces memory traffic
Smaller weights = faster transfer
Software overhead
Dequantization at runtime costs cycles
Fixed GPU architecture
Cannot adapt to outlier patterns
Solution: Custom hardware for quantized inference
6

## Slide 7
Software-Only Approach
Libraries like bitsandbytes let us run quantized models on standard GPUs
How Software Quantization Works
INT8 Weights
→
Dequantize
→
Compute
→
Output
The Dequantize step is overhead — GPU converts before every operation
Popular Frameworks
bitsandbytes: Tim Dettmers, INT8/INT4
ONNX Runtime: Microsoft, optimized INT8
llama.cpp: Georgi Gerganov, CPU
GPTQ: Post-training quantization
Fundamental Limitation
GPU hardware is designed for floating-point operations. We store as INT8 but must convert back to FP16 for every computation. This overhead can exceed the memory savings!
Key point: Software approaches work but cannot fully exploit quantization because the hardware is not designed for it.
7

## Slide 8
Software-Only Limitations
Finding: Quantization does not always speed things up — it depends on the implementation!
Framework
Precision
Platform
Speed
Result
bitsandbytes
INT8
GPU
0.65x
35% SLOWER
ONNX Runtime
INT8
GPU
1.7x
Good speedup
llama.cpp
INT4
CPU
0.3x
CPU limited
Why the Slowdown?
Dequantization overhead on every operation.
Memory access patterns not optimized.
GPU cores designed for FP, not INT.
Overhead can exceed memory savings.
The Core Problem
Software runs on fixed hardware.
No matter how clever our code, we are limited by what the GPU can physically do. We need hardware designed for quantized operations.
Bottom line: Software-only approaches cannot fully exploit quantization — the hardware is not designed for it.
8

## Slide 9
Research Focus
How do hardware-assisted quantization approaches compare to software-only methods in terms of performance and energy efficiency?
Approaches Compared
Software-Only
bitsandbytes, ONNX, llama.cpp
Oltron (ASIC)
DAC 2024, Peking University
FlightLLM (FPGA)
FPGA 2024, Tsinghua
Evaluation Metrics
Throughput, Energy Efficiency, Accuracy
Hypothesis
Hardware-assisted approaches will outperform software by eliminating dequantization overhead.
9

## Slide 10
Oltron: ASIC Approach
Algorithm-Hardware Co-design for Outlier-Aware Quantization
DAC 2024 · Peking University · Custom ASIC Accelerator
The Outlier Problem
Activation Value Distribution
Scale for normal values?
Normal 0.5 → 64 ✓ | Outlier 100 → OVERFLOW! X
Scale for outliers?
Outlier 100 → 127 ✓ | Normal 0.5 → rounds to 1 X
Oltron's insight: Outliers aren't random — they cluster in specific channels, and patterns vary by layer. Design hardware that adapts to each layer's outlier distribution.
Approach: Algorithm finds optimal outlier ratio per layer → Reconfigurable hardware adapts accordingly
10

## Slide 11
Oltron: Key Innovations
Three Core Innovations
INNOVATION 1
Adaptive Quantization
Analyze each layer's outlier distribution. Allocate INT4 vs FP16 precision per-channel based on sensitivity.
Layer 1: 2% FP16 | Layer 5: 15% FP16
INNOVATION 2
Reconfigurable PEs
Processing elements dynamically switch between INT4 and FP16 operations at runtime.
Hardware adapts to each layer's needs
INNOVATION 3
Tile-Based Dataflow
Reorganize memory access patterns to maximize data reuse and minimize bandwidth requirements.
Reduces memory bottleneck
Co-Design Principle: Algorithm determines optimal outlier ratio → Hardware reconfigures to match → Both work together for maximum efficiency
1.9×
Speedup
1.6×
Energy Efficiency
<1%
Accuracy Loss
12nm
Process Node
11

## Slide 12
Oltron: Results
Performance vs OliVe (Previous Best)
Metric
OliVe
Oltron
Improvement
Performance
1.0x
1.9x
1.9x faster
Energy Efficiency
1.0x
1.6x
1.6x better
Accuracy Loss
Baseline
Less than 1%
Maintained
Implementation
Process
12nm
Clock
500 MHz
Models
LLaMA, OPT
Why These Results?
Adaptive Quantization
Each layer optimized individually
Hardware Flexibility
No wasted compute cycles
Memory Efficiency
Tile-based layout reduces overhead
Co-Design Synergy
Algorithm + hardware working together
Takeaway: 1.9x speedup and 1.6x energy efficiency with less than 1% accuracy loss — the power of co-design
12

## Slide 13
FlightLLM: FPGA Approach
Efficient Large Language Model Inference with a Complete Mapping Flow on FPGAs
FPGA 2024 · Tsinghua and Shanghai Jiao Tong University · Xilinx U280
Why FPGA?
GPU Limitations
Fixed architecture: Cannot skip zero computations
Memory bottleneck: Must fetch from DRAM every token
High power: A100 draws 300-400W
FPGA Advantages
Reconfigurable fabric: Design custom compute paths
On-chip SRAM: 100x faster than DRAM
Lower power: Around 75W for similar work
FlightLLM insight: Design FPGA architecture specifically for sparse, quantized LLM inference — exploit sparsity, keep data on-chip, compile once and run any sequence length.
Target: Efficient decode phase — the bottleneck in real LLM serving (one token at a time)
13

## Slide 14
FlightLLM: Key Innovations
Three Core Innovations
INNOVATION 1
Configurable Sparse DSP
Custom DSP units that detect and skip zero-value computations entirely. No wasted cycles.
1.6× compute efficiency gain
INNOVATION 2
Always-On-Chip Decode
KV cache stored entirely in fast SRAM instead of slow DRAM. Eliminates memory bottleneck.
100× faster memory access
INNOVATION 3
Length-Adaptive Compile
Single compilation works for any sequence length. No recompilation needed for different inputs.
Handles 128 to 2048+ tokens
FPGA Advantage: Reconfigurable fabric enables sparsity exploitation + on-chip memory optimization — impossible on fixed GPU architecture
6×
Energy Efficiency
1.2×
vs A100 Throughput
75W
Power Draw
$5K
Xilinx U280
14

## Slide 15
FlightLLM: Results
Performance Comparison
Platform
Power
Throughput
Energy Eff.
V100S GPU
250W
1.0x (baseline)
1.0x
A100 GPU
300W
1.1x
0.9x
FlightLLM
75W
1.2x
6x better
Implementation
Hardware
Xilinx U280
Memory
8GB HBM2
Model
LLaMA-7B INT4
Power Comparison
A100
300W
V100S
250W
FlightLLM
75W
Bottom line: Same throughput as $15,000 A100, at 1/4 the power, on a $5,000 FPGA.
Takeaway: FPGA delivers GPU-level throughput at 1/4 the power — critical for sustainable deployment at scale
15

## Slide 16
Comparison: Software vs Hardware
Approach
Platform
Key Technique
Speedup
Energy Eff.
Software-Only
Standard GPU
Dequantize at runtime
0.65-1.7x
1x baseline
Oltron (ASIC)
Custom accelerator
Adaptive quantization
1.9x
1.6x
FlightLLM (FPGA)
Xilinx U280
Sparsity + on-chip mem
1.2x vs A100
6x
Software-Only Limitations
Fixed hardware cannot adapt to outliers
Dequantization overhead on every op
Cannot exploit sparsity efficiently
Hardware-Assisted Advantages
Native INT4/INT8 compute units
Reconfigurable for different layers
Memory architecture co-optimized
Trade-off: Software approaches are more accessible (standard GPUs), but hardware-assisted solutions deliver significantly better efficiency for production deployment
Conclusion: Co-design approach (algorithm + hardware together) consistently outperforms software-only solutions
16

## Slide 17
Future Work
1
Hands-On Implementation
Benchmark software quantization tools (bitsandbytes, llama.cpp) on local hardware to validate CipherCore findings
2
Emerging Hardware
Evaluate newer accelerators: Groq LPU, AWS Inferentia, Google TPU — all natively support quantized inference
3
Cost-Benefit Analysis
Total cost of ownership: GPU rental vs FPGA deployment vs custom ASICs at datacenter scale
Additional Research Direction
Combine Oltron's adaptive quantization with FlightLLM's sparsity exploitation — could yield even greater efficiency gains by addressing both outliers and zeros simultaneously
Course
These hardware approaches exemplify the memory hierarchy optimization, dataflow architecture, and hardware-software co-design concepts from our Advanced Computer Architecture curriculum
17

## Slide 18
Conclusion
Three Key Takeaways
1
Hardware Matters
LLM inference is memory-bound. Custom hardware eliminates dequantization overhead that limits software approaches.
2
Co-Design Wins
Algorithm + hardware designed together — Oltron's adaptive quant + reconfigurable PEs, FlightLLM's sparse DSPs.
3
Energy is Key
FlightLLM's 6x efficiency shows why specialized accelerators matter for sustainable AI deployment at scale.
Key Numbers to Remember
140 GB
LLaMA-70B memory
1.9x
Oltron speedup
6x
FlightLLM efficiency
75W
vs 300W GPU
References: Oltron (DAC 2024, Peking University) · FlightLLM (FPGA 2024, Tsinghua and SJTU) · CipherCore Benchmark Study
18

## Slide 19
Any Questions?
Hardware/Software Co-Design for LLM Quantization
1.9x
Oltron Speedup
6x
FlightLLM Efficiency
75W
vs 300W GPU
Gyanendra Pandey – CECS 530
6th December 2025
17